## Slide 1: Performance and Power Characterization of 3G/4G Networks and Optimizations of Mobile Applications
December 18, 2012
Candidate: Junxian Huang
Advisor: Z. Morley Mao

## Slide 2: Smartphone application performance and energy efficiency is key to user experience
AT&T
T-Mobile
Verizon

## Slide 3: Key problems for smartphone applications
Applications loading slow
Battery draining fast

## Slide 4: Challenges
Applications loading slow
Battery draining fast
Network performance not straightforward to quantify

## Slide 5: Challenges
Applications loading slow
Battery draining fast
Impact of cellular networks on device energy is not clear

## Slide 6: Problem statement
How can we make smartphone applications faster and energy efficient?
  To make them faster, we need to
    identify the bottleneck of application performance
      Quantify cellular network performance is one important step
    Optimize applications to make the network better utilized
  To make them more energy efficient, we need to
    Understand the impact of cellular networks on device energy consumption
    Optimize applications to improve energy efficiency
Notes: ----- Meeting Notes (12/18/12 10:42) -----
emphasize contributions
extract results to be aaa

## Slide 7: Roadmap
(Task 1) Understand the network performance and power characteristics of cellular networks and mobile applications
(Task 2) Optimize mobile application design to improve the energy efficiency
(Task 3) Optimize mobile application design to improve the network efficiency

## Slide 8: Task 1
(Phase 1) Between 2008 and 2010, we study the network performance of 3G networks [MobiSys 10]
(Phase 2) Since 2011, we study the network performance of LTE 4G networks
(Phase 3) Since 2011, we study the power characteristics of cellular networks
(Phase 4) Characterize smartphone application performance and energy efficiency

## Slide 9: Representativeness of 3GTest data
  66K+ users 148K+ runs 84 carriers 147 countries over 10 months
Notes: Why US only data? Fair comparisons?
3GTest is used for measuring the previous metrics globally
Take about what 3GTest app is like (client-server communication)
Cross-platform
Deployment method

## Slide 10: Insights from 3GTest results
3G downlink bandwidth is low (at that time)
  < 1Mbps
Local DNS server performance is good
  200 ms comparable to ping to 1st hop
Carrier network delay dominates end-to-end RTT
  End-end ping close to ping to 1st hop
Notes: DNS 200ms close to ping to first hop
Ping to first hop close to end-to-end RTT
Time of day at certain locations
Signal strength correlates with TCP performance to some extent (threshold)

## Slide 11: Task 1
(Phase 1) Between 2008 and 2010, we study the network performance of 3G networks
(Phase 2) Since 2011, we study the network performance of LTE 4G networks [MobiSys 12]
(Phase 3) Since 2011, we study the power characteristics of cellular networks
(Phase 4) Characterize smartphone application performance and energy efficiency

## Slide 12: LTE is new, requires exploration
4G LTE (Long Term Evolution) is future trend
  Initiated by 3GPP in 2004
    100Mbps DL, 50Mbps UL, <5ms latency
  Entered commercial markets in 2009 and now available in more than 10 countries
Notes: Before I came here, I was in New York City where I see many LTE advertisements saying super super fast speed, revolutions, blabla.
So what is LTE? Let me first give you a brief introduction.
LTE stands for Long Term Evolution. Back in 2004, 4G LTE is initiated by 3GPP.
The design goal for LTE is quite promising, with 100Mbps downlink, 50Mbps uplink and <5ms user-plane latency.
Since 2009, LTE has entered commercial markets and now available in more than 10 countries, with more countries ongoing or planned.
It is anticipated to become the first truly global mobile phone standard and is a future trend
==================================
Since LTE is the natural upgrade path for carriers with 3G networks,
we review some of the important lessons we learnt from 3G UMTS networks
In 3G network, the network maintains a state machine for each UE. UE stands for user equipment or handset.
The network stays synchronized with UE for state transitions.
This state machine is called Radio Resource Control state machine, or RRC state machine.
1 It is very important in determining the radio resource allocation and management.
2 The application traffic patterns would trigger state transitions, and the individual RRC states also determine the instant power consumption level for UE and user experience
3 The state transitions, especially state promotions from the idle state to high-power state, could incur overhead in energy, delay and signaling.

## Slide 13: LTE Network characteristics
4GTest on Android
  Measures network performance with the help of 46 M-Lab nodes across the world
  3,300 users and 14,000 runs in 2 months 10/15/2011 ~ 12/15/2011
4GTest user coverage in the U.S.
Notes: To make such large-scale measurement, we developed and published an app called 4GTest in Android market.
In order to make sure that the Internet path does not become the bottleneck, 4GTest chooses the closest M-Lab nodes to connect to, which are distributed across the world.
Within 2 months of deployment, we collect data from more than 3000 users
Based on this figure, we can see that our data set has a reasonably good coverage in the United States.

## Slide 14: LTE Network characteristics
4GTest on Android
  Measures network performance with the help of 46 M-Lab nodes across the world
  3,300 users and 14,000 runs in 2 months 10/15/2011 ~ 12/15/2011
4GTest user coverage in the U.S.
Notes: To make such large-scale measurement, we developed and published an app called 4GTest in Android market.
In order to make sure that the Internet path does not become the bottleneck, 4GTest chooses the closest M-Lab nodes to connect to, which are distributed across the world.
Within 2 months of deployment, we collect data from more than 3000 users
Based on this figure, we can see that our data set has a reasonably good coverage in the United States.

## Slide 15: Downlink throughput
LTE median is 13Mbps, up to 30Mbps
  The LTE network is relatively unloaded
WiFi, WiMAX < 5Mbps median
Notes: Comparing downlink throughput, LTE’s median throughout is 13Mbps, and for some users, it can be up to 30Mbps.
We need to notice that LTE network is currently relatively unloaded due to its new coming.
For WiFi and WiMAX, their median downlink throughput is smaller than 5Mbps. And 3G networks are lower.

## Slide 16: Uplink throughput
LTE median is 5.6Mbps, up to 20Mbps
WiFi, WiMAX < 2Mbps median
Notes: For uplink throughput, LTE’s median throughput is 5.6Mbps, which is also much higher than that of WiFi or WiMAX.

## Slide 17: RTT
LTE median 70ms
WiFi similar to LTE
WiMAX higher
Notes: For RTT, LTE and WiFi have similar median value of 70ms,
WiMAX and 3G networks have higher RTTs, and the median value is between 100ms and 200ms.

## Slide 18: Task 1
(Phase 1) Between 2008 and 2010, we study the network performance of 3G networks
(Phase 2) Since 2011, we study the network performance of LTE 4G networks
(Phase 3) Since 2011, we study the power characteristics of cellular networks [MobiSys 12]
(Phase 4) Characterize smartphone application performance and energy efficiency

## Slide 19: RRC state transitions in LTE
Notes: With the knowledge from the LTE specs and our local experiments,
we illustrate the LTE state machine and state transition procedures in this slide
There are two RRC states in LTE network, RRC_CONNECTED and RRC_IDLE.
Distinct states determine very different UE power consumption.

## Slide 20: RRC state transitions in LTE
RRC_IDLE
No radio resource allocated
Low power state: 11.36mW average power
Promotion delay from RRC_IDLE to RRC_CONNECTED: 260ms
Notes: In the RRC_IDLE state, there is no radio resource allocated and UE can’t receive/send any data.
UE is consuming very low average power at this state in the network interface, for example 11mW in our test device.
If there is any data transfer activity, there would be a state promotion from RRC_IDLE to a high power state: RRC_CONNECTED, and the measured promotion delay is 260ms in our test device, much smaller than that for 3G.

## Slide 21: RRC state transitions in LTE
RRC_CONNECTED
Radio resource allocated
Power state is a function of data rate:
  1060mW is the base power consumption
  Up to 3300mW transmitting at full speed
Notes: In the RRC_CONNECTED state, radio resource is allocated to a UE.
And the instant power level for UE is high, depending on data rate, it ranges from 1000mW to up to more than 3000mW when transmitting data at full speed.
If there is no data activity for some time, a timer would expire and it triggers the demotion from RRC_CONNECTED to RRC_IDLE

## Slide 22: RRC state transitions in LTE
Continuous Reception
Send/receive a packet
Promote to RRC_CONNECTED
Reset Ttail
Notes: Now, we will discuss the state transitions in LTE in more details
Initially, UE is in RRC_IDLE model, with no network resource allocated from the network.
When there is a packet to be sent or received, a state promotion from RRC_IDLE to RRC_CONNECTED would be triggered.
A timer called Ttail is reset at this time.
Ttail is the inactivity tail timer in LTE network, which controls how long UE stays in RRC_CONNECTED state after being idle

## Slide 23: RRC state transitions in LTE
Ttail stops
Demote to RRC_IDLE
DRX
Ttail expires
Notes: At RRC_CONNECTED state, after sending/receiving a packet, UE does not immediately go to RRC_IDLE.
Instead, UE keeps in RRC_CONNECTED state for some extra time. This extra time is called the tail time.
Ttail controls how long the tail time is.
When Ttail expires and UE demote to RRC_IDLE.

## Slide 24: Tradeoffs of Ttail settings
Ttail setting | Energy Consumption | # of state transitions | Responsiveness
Long | High | Small | Fast
Short | Low | Large | Slow
Notes: Ttail is a very important parameter for both 3G and 4G networks.
It incurs tradeoffs between UE energy consumption, signaling overhead in the network quantified by the # of state transitions here
, and responsiveness
When Ttail is set to be a long value, UE consumes more energy, with smaller # of state transitions and fast responsiveness since UE spends more time in the RRC_CONNECTED state and there is less promotion delays.
When Ttail is set to be a short value, UE consumes less energy, incurring larger number of state transitions and more promotions delays
Later in this talk, we will explore in more details the impact of setting Ttail for LTE network.

## Slide 25: Power trace of RRC state transitions
The data points are sampled and DRX in RRC_CONNECTED tail
is not obvious due to the low sampling rate
Notes: This figure shows the measured power trace of first uploading some data and then stays idle.
At time t1, when there is data to send, state promotion takes place and the power level jumps from very low to very high.
At time t2, data transmission starts and then depending on the instant data rate, the power level fluctuates.
At time t3, data transmission finished and the tail timer is started.
UE keeps in a high-power state until t4

## Slide 26: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: We notice that in the RRC_CONNECTED tail, for any DRX cycle, the power level of the off duration is 1060mW.
And the tail timer is measured to be 11.6seconds

## Slide 27: LTE consumes more instant power than 3G/WiFi in the high-power tail
Average power for WiFi tail
  120 mW
Average power for 3G tail
  800 mW
Average power for LTE tail
  1080 mW
Notes: We compare the instant tail power level of the three network types, since tail energy is the main source of wasted energy.
WiFi appears to be the least power consuming, only 120 mW.
3G tail has a high power level of 800 mW.
LTE has the even higher power level in RRC_CONNECTED mode, 1080 mW.
Considering that LTE tail timer is even longer than that for 3G in our measured network, more energy is wasted in the tail for LTE than 3G in that network.

## Slide 28: Power model for data transfer
A linear model is used to quantify instant power level:
  Downlink throughput td Mbps
  Uplink throughput tu Mbps
< 6% error rate in evaluations with real applications
Notes: In addition to the power states, we also use a simple linear model to quantify the
instant power level based on the data rates in uplink and downlink.
The higher the throughput, the higher the power.
It’s simple yet validated to be effective and accurate, with the error rate for the predicted energy usage of real applications to be < 6%.

## Slide 29: Power model for data transfer
A linear model is used to quantify instant power level:
  Downlink throughput td Mbps
  Uplink throughput tu Mbps
AT&T
Verizon
Notes: In addition to the power states, we also use a simple linear model to quantify the
instant power level based on the data rates in uplink and downlink.
The higher the throughput, the higher the power.
It’s simple yet validated to be effective and accurate, with the error rate for the predicted energy usage of real applications to be < 6%.

## Slide 30: Energy per bit comparison
LTE’s high throughput compensates for the promotion energy and tail energy
Transfer Size | LTE μ J / bit | WiFi μ J / bit | 3G μ J / bit
10KB | 170 | 6 | 100
10MB | 0.3 | 0.1 | 4
Total energy per bit for downlink bulk data transfer
Notes: In this table, we compare the energy per bit for the three networks in the downloading bulk data with different sizes.
For a small download of 10KB, LTE and 3G is clearly much more power consuming than WiFi, with LTE as 170 μJ/bit
However, when we download a large file of 10MB LTE’s high throughput compensates for the promotion energy and tail energy.
The energy per bit for LTE in this scenario is 0.3 μJ/bit, which is comparable to WiFi’s μJ/bit. While for 3G, it is much worse, with 4 μJ/bit.

## Slide 31: Energy per bit comparison
LTE’s high throughput compensates for the promotion energy and tail energy
Transfer Size | LTE μ J / bit | WiFi μ J / bit | 3G μ J / bit
10KB | 170 | 6 | 100
10MB | 0.3 | 0.1 | 4
Total energy per bit for downlink bulk data transfer
Small data transfer, LTE wastes energy
Large data transfer, LTE is energy efficient
Notes: So the high level observation for LTE network is that
It wastes energy for small data transfers,
But could become energy efficient for large data transfer.
For large data transfers, LTE has comparable energy efficiency compared with WiFi.

## Slide 32: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%
Notes: We future break down the energy usage into 4 components:
Promotion energy, data transfer energy, tail energy and idle energy.
We observe that tail energy takes up to 48% of the total energy for 3G and LTE network, while this problem does not exist in WiFi.

## Slide 33: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%
The tail problem is the key factor for LTE’s high energy consumption, similar to 3G networks
Notes: The tail problem is still the key factor for LTE high energy consumption, similar to 3G networks

## Slide 34: Task 1
(Phase 1) Between 2008 and 2010, we study the network performance of 3G networks
(Phase 2) Since 2011, we study the network performance of LTE 4G networks
(Phase 3) Since 2011, we study the power characteristics of cellular networks
(Phase 4) Characterize smartphone application performance and energy efficiency [MobiSys 10] [Mobisys 12]

## Slide 35: Smartphone web browsing is complicated
Smartphone
Local DNS server
Web server
DNS lookup
Content customization
TCP handshake
TCP data transfer
1
2
4
Server configuration
Client configuration
HTML rendering & JavaScript execution
5
Network condition
Server processing delay
3
Notes: (factors controlled network content server client VS. factors break down : + server delay)
Hard to quantitatively measure and break down web performance
  How to identify when a web page finishes loading?
  Server client configuration
  Dns handshake idle server processing deley
  Parallel TCP flows and concurrent HTML parsing and JavaScript execution
How is this different from desktop web browsing
Talk about different components in smartphone web browsing.
Emphasis the difficulty and importance of break down analysis
Bring out what we are doing later:
1 Measure 3G network performance
2 Study different factors

## Slide 36: Simple website page load time break down
http://m.ebay.com
TCP idle time
TCP transfer time
Notes: Compare left to right: performance gap among devices become more obvious for content-rich websites because TCP transfer time and idle time become more of a bottlenecks
Web bottlenecks: idle time and transfer time ( client exe + data download) not TCP handshake, DNS

## Slide 37: Content-rich website page load time break down
http://mapquest.com
TCP idle time
TCP transfer time
Notes: Compare left to right: performance gap among devices become more obvious for content-rich websites because TCP transfer time and idle time become more of a bottlenecks
Web bottlenecks: idle time and transfer time ( client exe + data download) not TCP handshake, DNS

## Slide 38: JavaScript execution comparison (2012)
From 2009 to 2012, smartphones have significantly improved JavaScript execution speed
Notes: We first revisited the smartphone processing capability analysis that we carried out in 2009.
To understand the smartphone’s processing capability, we use JavaScript execution speed as a representative metric.
The JavaScript benchmark suite we used is the same in 2009 and 2011.
In 2009, we found that the execution speed for smartphone browsers could be up to 20∼80 times slower than desktop browsers.
From 2009 to 201, there is a 20 – 50 times speed up for smartphone browsers.
And the gap between smartphones and computers has dropped to 5 ∼ 20 times in 2011.

## Slide 39: Lessons from application performance study
Performance bottlenecks of web browsing
  Client execution
  Data download
Higher concurrency significantly improves performance
Compression is usually helpful
Content customization is beneficial
  Data URL scheme
  Minification
  Minimal redirections
Notes: Major observations
Video player on Gphone and iPhone (for example)

## Slide 40: App case study in LTE networks
Studied 5 web-based apps
LTE has comparable page loading time as WiFi, with 3G lagging behind
CPU usage for LTE/WiFi is between 80% ~ 90% during page loading
  Network does not appear to be the bottleneck
Total energy consumption: LTE > 3G >> WiFi
Notes: We studied 5 web-based application in our test device and
here lists the most important lessons we learnt.
First, LTE has comparable loading time with WiFi for these applications, and 3G’s loading time is longer, as expected.
Second, we monitor the CPU usage, during the loading of these applications, in LTE and WiFi networks, the average CPU usage is between 80% to 90%.
This indicates that the network is less of a performance bottleneck, and the UE processing is the bottleneck, even though smartphone processing speed has significantly improved.
For 3G, the CPU usage is about 35% to 70%, indicating that network is more of a bottleneck.
In terms of the total energy consumed in loading these applications, LTE consumers more energy than 3G, and the two are much more energy consuming than WiFi.

## Slide 41: App case study in LTE networks
Studied 5 web-based apps
LTE has comparable page loading time as WiFi, with 3G lagging behind
CPU usage for LTE/WiFi is between 80% ~ 90% during page loading
  Network does not appear to be the bottleneck
Total energy consumption: LTE > 3G >> WiFi
In LTE networks, applications should more aggressively burst traffic to make more efficient use of the bandwidth given the high energy overhead
Notes: All these lesson implies that, when designing smartphone applications that include network activities,
The guideline is that, for LTE network, since it provides a very high network throughput at the cost of high energy usage,
Applications should more aggressively burst traffic and reduce periodic small data transfers whenever possible.
This helps make better use of the available bandwidth and saves UE energy

## Slide 42: Roadmap
(Task 1) Understand the network performance and power characteristics of cellular networks and mobile applications
(Task 2) Optimize mobile application design to improve the energy efficiency
(Task 3) Optimize mobile application design to improve the network efficiency

## Slide 43: Task 2
(Phase 1) Optimize screen-off traffic to reduce UE energy consumption [IMC 12]
(Phase 2) Predict traffic pattern based on recent history and make intelligent decisions on releasing resources earlier to save UE energy

## Slide 44: Screen-off traffic characterization: an interesting yet unexplored topic
Smartphone screen is switched on and off often (>50 times/day/user)
Screen status is a good heuristic for determining whether the user is actively interacting with the device
Battery is scarce resource for smartphones
Notes: Screen-off traffic characterization is an interesting yet unexplored topic.
Here “screen-off” means switching the screen the off and putting the smartphone into standby mode, rather than meaning shutting down the phone
I’m not sure whether any of you have ever counted how many time you switch the screen on and off,
We observe that
For some users, this number reaches up to hundreds

## Slide 45: Screen-off traffic characterization: an interesting yet unexplored topic
Smartphone screen is switched on and off often (>50 times/day/user)
Screen status is a good heuristic for determining whether the user is actively interacting with the device
Battery is scarce resource for smartphones
Notes: and users do not want the battery drain too much when the screen is off

## Slide 46: Breakdown of packet count based on screen status
Chart: 
| Packet count
Screen-on | 55.13
Screen-off | 35.84
Unknown | 9.02
Unknown group: 9% of all packets, due to users
accidentally terminating screen status logger
50%
%
Notes: The breakdown of packet count based on screen status is shown as below

## Slide 47: Breakdown of packet count based on screen status
Chart: 
| Packet count
Screen-on | 55.13
Screen-off | 35.84
Unknown | 9.02
Unknown group: 9.02% of all packets, due to users
accidentally terminating screen status logger
50%
36% screen-off packets
Could be more given the unknown category
What is their energy and signaling impact?
Notes: Highlight that screen-off packet count is high

## Slide 48: Screen-on and screen-off traffic comparison
Screen-off traffic has less packets/payload, but more bursts which are smaller and shorter
Chart: 
| Packet number | Payload | Burst number
Screen-on | 55.13 | 64.31 | 22.2326
Screen-off | 35.84 | 27.26 | 65.2674
Unknown | 9.03 | 8.43 | 12.5
%
Notes: We first look at the aggregate traffic characteristics comparison between screen-on and screen-off traffic.
First, in terms of the % of all packets, …
Implication of these observations

## Slide 49: Does screen-off traffic matter for radio resource and energy?
Yes! Actually, screen-off traffic has higher impact than screen-on, though with less packets
Chart: 
| Screen-on | Screen-off | Unknown
Energy | 0.2218 | 0.5855 | 0.1927
Chart: Signaling overhead
| Screen-on | Screen-off | Unknown
Energy | 0.1487 | 0.5803 | 0.271
Notes: We then compare the radio and energy impact between screen-on and screen-off traffic
At least 59%, and unknown can even contribute to more screen-off energy

## Slide 50: Screen-aware traffic optimization
Apply more aggressive settings to screen-off traffic
  Reason 1: high energy and signaling impact
  Reason 2: traffic pattern is more “scattered”
  Reason 3: less user interaction and more tolerance in delay
Notes: Given that the screen-off traffic consumes significant amount of UE energy and radio resources,

## Slide 51: Case study: screen-aware fast dormancy
Fast dormancy reduces the tail length by actively notifying the network for early demotion
Fast dormancy
51
Time
Power
Default tail timer
Fast dormancy
tail timer
Notes: As case study, we first study fast dormancy, which is a technique to allow UE to demote to low power state faster by actively notifying the network.

## Slide 52: Case study: screen-aware fast dormancy
Fast dormancy reduces the tail length by actively notifying the network for early demotion
Fast dormancy
52
Time
Power
Screen-aware fast dormancy: a shorter tail timer for screen-off traffic
For the same signaling overhead, screen-aware fast dormancy increases energy saving by 15% compared with basic fast dormancy

## Slide 53: Summary
Screen-off traffic incurs more energy overhead, with fewer packets and less payload than screen-on traffic
Screen-aware optimization improves the resource efficiency and is simple to implement
Other screen-aware traffic optimization techniques studied in the paper, e.g., batching

## Slide 54: Task 2
(Phase 1) Optimize screen-off traffic to reduce UE energy consumption
(Phase 2) Predict traffic pattern based on recent history and make intelligent decisions on releasing resources earlier to save UE energy [In submission to EuroSys 13]

## Slide 55: RadioProphet: Intelligent Radio Resource Deallocation for Cellular Networks
Notes: We have done initial work on this project to demonstrate the effectiveness of the idea.
However, we have not fully implemented the RadioProphet system in real devices yet.

## Slide 56: Example feature selection – TCP flags
Notes: For SYN, PSH/ACK packets, clear indication of short burst

## Slide 57: Initial evaluation
Prediction accuracy 85.88% for all applications’ mixed traffic
Achieves radio energy saving by 59.07%, at the cost of 91.01% additional signaling overhead in LTE networks, outperforming previous proposals
Real implementation on Android and evaluation is future work

## Slide 58: Roadmap
(Task 1) Understand the network performance and power characteristics of cellular networks and mobile applications
(Task 2) Optimize mobile application design to improve the energy efficiency
(Task 3) Optimize mobile application design to improve the network efficiency
  Deadline Feb 1, 2013

## Slide 59: Task 3
(Phase 1) Devise methods to estimate and predict available bandwidth, and study the network efficiency of existing mobile applications
(Phase 2) Study practical ways to improve the network efficiency and implement in real-world applications

## Slide 60: Bandwidth estimation in cellular networks
Packet train based algorithm to estimate bandwidth with server/network side traces
Initial observations
  Available bandwidth changes frequently in the order of seconds
  Using a larger time window reduces the throughput variation

## Slide 61: Questions to explore
Is available bandwidth predictable?
  Based on history samples
  Considering signal strength in addition
  Which time windows results in highest predictability?

## Slide 62: Network efficiency of existing mobile applications
Data set
  Packet traces collected in AT&T’s LTE network for 10 days, 500GB in total consisting ~ 200,000 users
Characterize network efficiency of different applications and different users
Identify suboptimal application design which results in low network efficiency

## Slide 63: Task 3
(Phase 1) Study the network efficiency of existing mobile applications and devise methods to estimate and predict available bandwidth
(Phase 2) Study practical ways to improve the network efficiency and implement in real-world applications

## Slide 64: Improving TCP/HTTP for cellular networks
Is there any inefficiencies incurred by the design of TCP/HTTP?
If available bandwidth is predictable, how does TCP/HTTP benefit from it?
If not, how to make TCP/HTTP adjust to fast-changing available bandwidth to make better use of the network capacity?

## Slide 65: Thank you! && Happy Holidays!
Notes: Thank you and I’m glad to take questions!

## Slide 66: Backup slides

## Slide 67: Smartphones are popular
Various smartphone platforms
Many applications
High speed network access
  3G (UMTS & EVDO)
  4G (LTE)

## Slide 68: Smartphone shipments prediction on 2009
Predicted on 2009: 2012 Global smartphone shipments 385 million

## Slide 69: Smartphone shipments booming
2012 Global smartphone shipments: 717 million
How about 2016?

## Slide 70: Design of 3GTest
Avoid personal identifiable information
http://mobiperf.com
Notes: Avoid personal identifiable information
Limit running time
Simple UI with one click to run
Leave users the option to run once or multiple times

## Slide 71: Key challenges of 3GTest design – public tool to measure 3G network performance
Adoptability
  User privacy
  Running time
  Ease of use
  Energy consumption
Data usefulness
  Metrics relevant to network applications
Notes: Talk about the challenges and our solutions
To extract important network metrics and understand network properties
To measure the network metrics globally to analyze commonalities and compare differences.

## Slide 72: What information is most relevant for 3GTest?
Smartphone
Local DNS server
Web server
example.com?
192.0.32.10
Get index.html
<html></html>
Ping to 1st hop
End-end ping
Notes: DNS performance
  Local DNS lookup time
TCP performance
  Throughput
  RTT
  Loss rate
Ping performance
  Latency to landmark servers
  Latency to the first hop

## Slide 73: Throughput comparison
CDF
T-Mobile:600kbps
AT&T
1Mbps
Notes: 1, variation within each carrier
2, common throughput values
3, ATT > T-Mobile

## Slide 74: RTT comparison
CDF
T-Mobile
450ms
AT&T
350ms
Notes: 1, variation within each carrier
2, common RTT values 400ms (higher than Internet values)
3, ATT > T-Mobile (T-Mobile has high RTT)

## Slide 75: Retransmission rate comparison
CDF
T-Mobile
AT&T
Notes: 1, common retransmission values
2, UMTS vs. EVDO (possibly due to link-layer retransmission
Link-layer retransmission for low loss rate

## Slide 76: Ping to the first hop

## Slide 77: Ping to end server

## Slide 78: Time of day effect on network performance

## Slide 79: JavaScript execution comparison (2009)
PC
80X (CPU <10X)
Notes: Background: choose to use JavaScript because it is the most common scripts which require client processing
PC vs. smartphone difference is big (js is expensive on smartphones, content providers need to optimize contents)
Difference among different smartphones are big
Possible reasons include CPU speed difference and JS engine software performance difference

## Slide 80: Interesting questions about LTE
To users: what is the end performance?
  Network performance, such as RTT and throughput, how it compares with WiFi, 3G and WiMAX, etc.
  Energy efficiency affecting battery life, is LTE more power efficient than 3G or WiFi?
To ISPs: what is the impact of configuring LTE-related parameters on UE power saving, and delay/signaling overhead?
To OS/application developers: what is the performance bottleneck of applications in LTE network, CPU or network speed?
Notes: Given the previous discussion on LTE networks, in this study,
We raise some interesting questions about LTE network that are of interest of users, mobile ISPs and OS/application developers.
For users, they are interested to understand the network performance of LTE network and how it compares to other technologies, such as 3G, WiFi, WiMAX, etc.
For ISPs, the impact of configuring LTE-related parameters on energy saving and delay and signaling overhead is yet to be studied.
For OS and application developers, we want to study how the new LTE network would affect the application design
And what the is the performance bottleneck of mobile applications is it CPU or network speed.
(Merge with the first transition slide)

## Slide 81: RRC state transitions in LTE
DRX: Discontinuous Reception
Listens to downlink channel periodically for a short duration and sleeps for the rest time to save energy at the cost of responsiveness
Notes: Discontinuous reception, or DRX, is an important feature in LTE for energy saving purpose.
Instead of continuous monitoring downlink channel, in DRX, UE only listens to downlink channel periodically for a short duration, and sleeps for the rest time to save energy at the cost of responsiveness.

## Slide 82: Discontinuous Reception (DRX): micro-sleeps for energy saving
In LTE 4G, DRX makes UE micro-sleep periodically in the RRC_CONNECTED state
  Short DRX
  Long DRX
DRX incurs tradeoffs between energy usage and latency
  Short DRX – sleep less and respond faster
  Long DRX – sleep more and respond slower
In contrast, in UMTS 3G, UE is always listening to the downlink control channel in the data transmission states
Notes: We explain DRX in more details here.
In LTE 4G networks, DRX makes UE micro-sleep periodically in RRC_CONNECTED state.
There are two types of DRX in RRC_CONNECTED, Short DRX and Long DRX.
Different types of DRX incurs tradeoffs between battery saving and latency.
Short DRX sleeps slightly less with smaller energy saving and respond faster
Long DRX, sleeps more with more energy saving and respond slower.
The DRX in the data transmission state is one major difference between 3G and LTE.
In UMTS 3G networks, during the data transmission states, UE is continuously listening to the downlink control channel

## Slide 83: DRX in LTE
A DRX cycle consists of
  ‘On Duration’ - UE monitors the downlink control channel (PDCCH)
  ‘Off Duration’ - skip reception of downlink channel
Ti: Continuous reception inactivity timer
  When to start Short DRX
Tis: Short DRX inactivity timer
  When to start Long DRX
Notes: Now let’s look at DRX with a microscope.
DRX is periodic and each DRX cycle consists of
‘On Duration’ during which UE monitors the downlink control channel
‘Off Duration’ during which UE can sleep and skip the reception of downlink channel for battery saving purpose.
The On Duration is typically much smaller than the Off Duration so as to make effective energy saving
First, let’s start from the red dots where the UE starts transferring data.
Every time a packet is sent or received, the continuous reception inactivity timer Ti is started.
And when Ti expires, UE starts short DRX.
Then the short DRX inactivity timer Tis starts and when Tis expires without seeing any data, long DRX starts.

## Slide 84: RRC state transitions in LTE
Continuous Reception
Send/receive
a packet
Reset Ti
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 85: RRC state transitions in LTE
Short DRX
Ti stops, Tis starts
Ti expires
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 86: RRC state transitions in LTE
Continuous Reception
Send/receive
a packet
Reset Ti, stops Tis
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 87: RRC state transitions in LTE
Long DRX
Tis stops
Tis expires
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 88: RRC state transitions in LTE
Reset Ti
Continuous Reception
Send/receive
a packet
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 89: Power trace of DRX in RRC_CONNECTED
Notes: This figure is a zoom-in view of the power traces in RRC_CONNECTED model.
We can observe an obvious periodic behavior of DRX and around every 40ms
UE wakes up to check the downlink control channel for a very short period and goes back to sleep again.
To point to the difference

## Slide 90: One way delay and impact of packet size
LTE uplink one way delay (OWD) is larger than that of downlink
RTT in LTE is more sensitive to packet size than WiFi, mainly due to uplink OWD

## Slide 91: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: We measure the LTE power model with our test device and Monsoon power meter.
And we take the average with repeated samples.
All the energy are measured with screen turned off.

## Slide 92: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: As a reference for comparison, we measure the power level when the device is doing nothing but with the screen 100% on.
The power level is around 850 mW.

## Slide 93: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: For DRX on duration, the power level is even higher, up to 1680mW.

## Slide 94: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
P(on) – P(off) = 620mW, DRX saves 36% energy in RRC_CONNECTED
High power levels in both On and Off durations in the DRX cycle of RRC_CONNECTED
Notes: We make two interesting observations out of this table.
First, we notice that the DRX on duration has a higher power level than that of the off duration and
The gap between on and off is 620mW. This large gap allows the DRX to save 36% energy in RRC_CONNECTED state.
So DRX is effective.
Second, both on and off durations in the DRX cycle of RRC_CONNECTED, have high power levels.
So even though DRX helps save significant amount of energy, LTE still has high energy consumption in RRC_CONNECTED state.
This observation suggests that the high-power tail might still be a key source of energy inefficiency of LTE network as it is in 3G network.

## Slide 95: Power model for data transfer
A linear model is used to quantify instant power level:
  Uplink/downlink throughput tu/td (Mbps)
< 6% error rate for predicting energy usage of 5 real applications

## Slide 96: Energy per bit comparison
For large data transfer with maximum rate, LTE’s energy efficiency is comparable with WiFi, due to LTE’s high downlink throughput
Notes: Add comparison between WiFi and LTE’s absolute power levels.
The result in this slide is not general, because WiFi has < 6Mbps.
Probably remove this figure.
Add back this slides, remove the figure, put numbers.
Useful for bundle the data transfer

## Slide 97: LTE power model AT&T (New Jersey)

## Slide 98: LTE power model AT&T (Michigan)

## Slide 99: User trace based analysis
UMICH data set
  Collected from 20 volunteer smartphone users for five months, totaling 118GB
  Contains packet traces including full payload
Trace-driven modeling methodology
  Network model simulator
    Simulates network states, such as RRC state transitions
  Power model simulator
    Calculates power usage based on the network states
Notes: The approach we took for such comparison is the user trace based simulation analysis.
The data set we have is collected from 20 volunteer smartphone users for 5 months.
It contains packet traces with full payload.
We feed these traces into our network model simulator which simulates RRC state transitions
and power model simulator which is used to calculate energy usage based on the different network states.
This approach is not perfect since it is inherently challenging to replay user behaviors in different networks, especially when remote entities have been involved.
However, we believe that this approach provides a representative comparison for the energy efficiency of different networks.

## Slide 100: Comparing total energy of all user traces via simulation in LTE/3G/WiFi
Total energy usage
  LTE/WiFi ≈ 23 3G/WiFi ≈ 15
Notes: We first compare the total energy usage of all user traces.
In this figure, blue bars represent the energy ratio of LTE and WiFi
And red bars represent the energy ratio of 3G and WiFi.
In aggregate, we observe that LTE consumes up to 23 times the energy of WiFi, while 3G is 15 times of WiFi.
Across users, the ratio changes, but the overall pattern is consistent for all users.

## Slide 101: Design tradeoff in smartphone measurement
User coverage vs. collected information
User coverage
More info
Fewer users
Less info
More users
Collected information
Speedtest.net
FCC’s broadband test
Liu, MobiCom 2008
Zhong, HotMetrics 2010
Willkomm, DySPAN 2008
Our study
Notes: Discuss tradeoff: jailbroken / user privacy

## Slide 102: Key challenges of web performance analysis
Multiple factors have impact
  Network condition
  Client settings
  Server configurations
  Content differences
Lack of low-level information and access
  No visibility into link layer
  Difficult to instrument client OS and application
  No access to public web servers
Notes: 1 because various factors have joint impact

## Slide 103: How to isolate impact of individual factor?
Vary one factor at a time
  Network condition
    Simulate cellular network with WiFi
  Client settings
    Control TCP concurrency
  Server configurations
    Change compression mode and server parallelism
  Content difference
    Host static website snapshots locally
Notes: Present our solutions
each of which solves one problem in the problem statement
assume WiFi's performance is predictable due to a lack of contention.
WiFi has higher performance so you can create bottlenecks to emulate 3G.

## Slide 104: How to identify performance bottlenecks?
TCP flow analysis technique to break down page load time
  DNS lookup time
  TCP handshake time
  TCP idle time
  TCP transfer time
index.html
logo.png
Time
Notes:   DNS lookup time – local DNS server lookup time
  TCP handshake time - RTT
  TCP idling time - client execution time
  TCP transfer time - network performance & server delay

## Slide 105: Controlled experiment setup
Platform
Web browsing
Notes: Talk about the carrier and devices used for controlled experiments
20 URLs include mail, search engines, social networks, maps.

## Slide 106: Data set studied
Collected from 20 volunteers in 5 months
  May 2011 ~ Oct 2011, Android 2.2 smartphones
Full packet payload and process association is collected
  131.49 millions packets
  80.03GB payload
Screen on/off status with sampling rate of 1Hz
Notes: To study the screen-off traffic, we use a data set …
…
When we first got the data set, we are curious how many packets are generated during the screen-off stage

## Slide 107: Definition of a “burst”
A burst is a sequence of packets with inter-packet time ≤ BT, and leading/trailing gap > BT
BT is burst threshold selected empirically based on network RTTs, e.g. BT = 2s
> BT
> BT
≤ BT
…
≤ BT
Burst
Notes: One term we use in this study is burst.
A burst is …
For the same number of packets, if there are more bursts, the traffic pattern is more scattered.

## Slide 108: Radio Resource Control (RRC) state machine
Tail
Time
Promotion
Power
Transfer
the packet
A packet to
transfer
Tail timer
starts
Tail timer
expires
Notes: To understand the energy and signaling impact of network traffic, we review the Radio resource control state machines in cellular networks, or RRC state machines.

## Slide 109: How does traffic pattern affect energy and radio resource?
Scattered traffic consumes more energy and radio resource than Gathered traffic
Scattered
traffic
Gathered
traffic
Time
Power
Notes: Radio resource control state machine is important in determining cellular radio resource usage and UE energy consumption.
We need to understand two terms used in this study.
Promotion is …
Tail is defined to be the period that UE continus to stay in the high-power state

## Slide 110: Top screen-off applications based on packet count
Application category | screen-off packets / total packets
Homescreen widget | 3.80%
Multimedia streaming | 3.30%
Utility | 2.69%
Multimedia streaming | 2.66%
Multimedia streaming | 2.37%
Utility | 2.07%
Social network | 1.95%
News | 1.94%
Email | 1.33%
Notes: We then explore which application or progress generates most of the screen-off packets
Group app names into category
But having a large number of packets does not mean a big impact on energy consumption and signaling overhead

## Slide 111: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Notes: We further investigate the energy impact of top screen-off processes.
In the table, red bar represents the energy overhead, blue bar represents the burst count.
We can observe clear differences among applications.
We classify the applications to be 2 groups, based on their traffic pattern, the scattered group and the gathered group.
Comparing the two groups, we notice that although the total number of packets are comparable, scattered group includes significantly higher number of bursts incurring high energy impact.

## Slide 112: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Notes: Comparing these two applications

## Slide 113: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Traffic pattern has significant impact on resource consumption
    1.95% packets + 5% energy (Scattered)
    2.37% packets + 0.1% energy (Gathered)
Notes: For example, the screen-off traffic of one social network app consumes 5% of the total energy of applications in both screen-on and screen-off stages.
However, another multimedia streaming app with more screen-off packets consumes only 0.1% of the total energy.

## Slide 114: Object bundling
Bundling objects requested by the same client and transferring in one single bundle helps improve energy and network efficiency
Where to bundle? Server? Cellular core network? Cell tower?
How to bundle? Proactively or on demand?
How to quantify benefits?