## Slide 1: Performance and Power Characterization of Cellular Networks and Mobile Application Optimizations
Candidate: Junxian Huang
Advisor: Z. Morley Mao
April 25, 2013

## Slide 2: Smartphone ecosystem
Customer
Smartphone
Vendors
Application
Developers
Mobile
Carriers
Content
Providers
Slow!
Out of battery!
Notes: Customer is centered by a, b, c, d
Customer wishes to have the applications running on their smartphones be fast and energy efficient.
Smartphone vendors want to optimize the smartphone hardware and OS design to enable good user experience.
Application developers want to attract more users to boost their revenue
Mobile carriers, such as AT&T, Verizon, T-Mobile want to provide good network performance to users, without their network being overloaded and incurring high cost.
Content providers wish to optimize their content design to attract more users as well.

## Slide 3: Key motivations
Performance and power characteristics of cellular networks and smartphone applications are not well studied
  especially for the new LTE networks
Many smartphone applications are not well designed with inefficient use of network, radio and power resources
  mainly due to the unawareness of the cellular specific characteristics

## Slide 4: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 5: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 6: Design goals of MobiPerf
Measure most relevant network characteristics of cellular networks
Measurement results not be affected by any external factors
Attract a large number of users covering different carriers and geographical regions
Benefit the research community in terms of both tool and data

## Slide 7: Cellular network metrics
DNS (domain resolution)
  Local DNS response time
TCP
  Common TCP metrics: downlink/uplink throughput, round-trip time (RTT), packet loss rate, etc.
  For TCP throughput test, we choose the closest nodes among the 120+ global M-Lab nodes
Smartphone
Web server
Local DNS server
Notes: Talk about why we choose these metrics
DNS – DNS lookup
TCP – Web download, TCP is the most prevalent protocol used in cellular networks.

## Slide 8: Cellular network metrics
Ping (Impact of diverse Internet servers)
  Ping A: Ping latency to the first responsive IP hop
  Ping B: Ping latency to landmark servers at diverse Internet locations
Ping A
Ping B
Notes: Ping, Internet servers are at diverse locations.
Understanding this impact is important
This graph illustrates the infrastructure of 3G networks

## Slide 9: http://mobiperf.com

## Slide 10: Coverage of MobiPerf data
  70K+ users 200K+ runs 84 carriers 147 countries

## Slide 11: MobiPerf benefits the research community
Open source
  https://github.com/Mobiperf/MobiPerf
  Other researchers can easily add modular measurement tasks into MobiPerf tool
Open data
  gs://openmobiledata_public (Google storage)
Recognition
  2011, People's Choice Award and Open Internet App Reward in the FCC Open Internet Apps Challenge

## Slide 12: Insights of 3G network performance
3G downlink bandwidth is low
  < 1Mbps
Common 3G network condition
  RTT 400ms and loss rate 0%
Local DNS server performance is good
  200 ms comparable to ping to 1st hop
Carrier network delay dominates end-to-end RTT
  End-end ping close to ping to 1st hop
High variation
  Across carriers, and among the same carrier
  Within one TCP connection
Notes: DNS 200ms close to ping to first hop
Ping to first hop close to end-to-end RTT
Time of day at certain locations
Signal strength correlates with TCP performance to some extent (threshold)

## Slide 13: TCP RTT comparison across carriers
RTT of each carrier has high variation
400ms can be selected as a common RTT in 3G networks
Notes: RTT common value for 3G networks

## Slide 14: LTE is new, requires exploration
4G LTE (Long Term Evolution) is future trend
  Initiated by 3GPP in 2004
    100Mbps DL, 50Mbps UL, <5ms latency
  Entered commercial markets in 2009 and now available in more than 10 countries
Notes: Before I came here, I was in New York City where I see many LTE advertisements saying super super fast speed, revolutions, blabla.
So what is LTE? Let me first give you a brief introduction.
LTE stands for Long Term Evolution. Back in 2004, 4G LTE is initiated by 3GPP.
The design goal for LTE is quite promising, with 100Mbps downlink, 50Mbps uplink and <5ms user-plane latency.
Since 2009, LTE has entered commercial markets and now available in more than 10 countries, with more countries ongoing or planned.
It is anticipated to become the first truly global mobile phone standard and is a future trend
==================================
Since LTE is the natural upgrade path for carriers with 3G networks,
we review some of the important lessons we learnt from 3G UMTS networks
In 3G network, the network maintains a state machine for each UE. UE stands for user equipment or handset.
The network stays synchronized with UE for state transitions.
This state machine is called Radio Resource Control state machine, or RRC state machine.
1 It is very important in determining the radio resource allocation and management.
2 The application traffic patterns would trigger state transitions, and the individual RRC states also determine the instant power consumption level for UE and user experience
3 The state transitions, especially state promotions from the idle state to high-power state, could incur overhead in energy, delay and signaling.

## Slide 15: Downlink throughput
LTE median is 13Mbps, up to 30Mbps
  The LTE network is relatively unloaded
WiFi, WiMAX < 5Mbps median
Notes: Comparing downlink throughput, LTE’s median throughout is 13Mbps, and for some users, it can be up to 30Mbps.
We need to notice that LTE network is currently relatively unloaded due to its new coming.
For WiFi and WiMAX, their median downlink throughput is smaller than 5Mbps. And 3G networks are lower.

## Slide 16: Uplink throughput
LTE median is 5.6Mbps, up to 20Mbps
WiFi, WiMAX < 2Mbps median
Notes: For uplink throughput, LTE’s median throughput is 5.6Mbps, which is also much higher than that of WiFi or WiMAX.

## Slide 17: RTT
LTE median 70ms
WiFi similar to LTE
WiMAX higher
Notes: For RTT, LTE and WiFi have similar median value of 70ms,
WiMAX and 3G networks have higher RTTs, and the median value is between 100ms and 200ms.

## Slide 18: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 19: Smartphone web browsing is complicated
Smartphone
Local DNS server
Web server
DNS lookup
Content customization
TCP handshake
TCP data transfer
1
2
4
Server configuration
Client configuration
HTML rendering & JavaScript execution
5
Network condition
Server processing delay
3
Notes: (factors controlled network content server client VS. factors break down : + server delay)
Hard to quantitatively measure and break down web performance
  How to identify when a web page finishes loading?
  Server client configuration
  Dns handshake idle server processing deley
  Parallel TCP flows and concurrent HTML parsing and JavaScript execution
How is this different from desktop web browsing
Talk about different components in smartphone web browsing.
Emphasis the difficulty and importance of break down analysis
Bring out what we are doing later:
1 Measure 3G network performance
2 Study different factors

## Slide 20: Simple website page load time break down
http://m.ebay.com
TCP idle time
TCP transfer time
Notes: Compare left to right: performance gap among devices become more obvious for content-rich websites because TCP transfer time and idle time become more of a bottlenecks
Web bottlenecks: idle time and transfer time ( client exe + data download) not TCP handshake, DNS

## Slide 21: Content-rich website page load time break down
http://mapquest.com
TCP idle time
TCP transfer time
Notes: Compare left to right: performance gap among devices become more obvious for content-rich websites because TCP transfer time and idle time become more of a bottlenecks
Web bottlenecks: idle time and transfer time ( client exe + data download) not TCP handshake, DNS

## Slide 22: JavaScript execution comparison (2012)
From 2009 to 2012, smartphones have significantly improved JavaScript execution speed
Notes: We first revisited the smartphone processing capability analysis that we carried out in 2009.
To understand the smartphone’s processing capability, we use JavaScript execution speed as a representative metric.
The JavaScript benchmark suite we used is the same in 2009 and 2011.
In 2009, we found that the execution speed for smartphone browsers could be up to 20∼80 times slower than desktop browsers.
From 2009 to 201, there is a 20 – 50 times speed up for smartphone browsers.
And the gap between smartphones and computers has dropped to 5 ∼ 20 times in 2011.

## Slide 23: Lessons from application performance study
Performance bottlenecks of web browsing
  Client execution
  Data download
Higher concurrency significantly improves performance
Compression is usually helpful
Content customization is beneficial
  Data URL scheme
  Minification
  Minimal redirections
Notes: Major observations
Video player on Gphone and iPhone (for example)

## Slide 24: App case study in LTE networks
Studied 5 web-based apps
LTE has comparable page loading time as WiFi, with 3G lagging behind
CPU usage for LTE/WiFi is between 80% ~ 90% during page loading
  Network does not appear to be the bottleneck
Total energy consumption: LTE > 3G >> WiFi
Notes: We studied 5 web-based application in our test device and
here lists the most important lessons we learnt.
First, LTE has comparable loading time with WiFi for these applications, and 3G’s loading time is longer, as expected.
Second, we monitor the CPU usage, during the loading of these applications, in LTE and WiFi networks, the average CPU usage is between 80% to 90%.
This indicates that the network is less of a performance bottleneck, and the UE processing is the bottleneck, even though smartphone processing speed has significantly improved.
For 3G, the CPU usage is about 35% to 70%, indicating that network is more of a bottleneck.
In terms of the total energy consumed in loading these applications, LTE consumers more energy than 3G, and the two are much more energy consuming than WiFi.

## Slide 25: App case study in LTE networks
Studied 5 web-based apps
LTE has comparable page loading time as WiFi, with 3G lagging behind
CPU usage for LTE/WiFi is between 80% ~ 90% during page loading
  Network does not appear to be the bottleneck
Total energy consumption: LTE > 3G >> WiFi
In LTE networks, applications should more aggressively burst traffic to make more efficient use of the bandwidth given the high energy overhead
Notes: All these lesson implies that, when designing smartphone applications that include network activities,
The guideline is that, for LTE network, since it provides a very high network throughput at the cost of high energy usage,
Applications should more aggressively burst traffic and reduce periodic small data transfers whenever possible.
This helps make better use of the available bandwidth and saves UE energy

## Slide 26: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 27: Motivations
LTE has not been extensively studied empirically in a deployed commercial network setting
Study how network resources are utilized across different protocol layers for real users
Evaluate the benefits of increased bandwidth for mobile applications and essential network protocols to identify their limitations

## Slide 28: LTE network topology of the studied carrier

## Slide 29: LTE network topology of the studied carrier
Data collection point

## Slide 30: Data set studied
Data set statistics
  Covering a fixed set of 22 eNBs at a large metropolitan area in the U.S.
  Over 300,000 users
  3.84 billion packets, corresponding to 2.9 TB of LTE traffic
  Collected over 10 consecutive days
Data contents: packet header trace consisting of
  IP and transport-layer headers
  A 64-bit timestamp for each packet
  No payload data is captured except for headers of HTTP

## Slide 31: Highlight observations
TCP flow size exhibiting strong heavy-tail distributions, similar to wired networks
  90% flows < 3 KB uplink, < 36 KB downlink payload
  Top 0.6% of flows have 62% total downlink bytes
Delaying FIN/RESET for longer than 10 seconds occurs in 23% of the flows
TCP concurrency is not high
  1 TCP flow actively downloading for 72% of the time
In 2G/3G networks, usually the RAN latency dominates the overall end-to-end delay; no longer the case in LTE networks

## Slide 32: Breakdown of content type for all HTTP traffic based on content size
Video and image contents are dominant

## Slide 33: Queueing delay
Large buffers in the LTE networks may cause high queuing delays
Bytes in flight – unacknowledged TCP bytes

## Slide 34: High queueing delay causes unexpected TCP behavior
When one LTE user is downloading data …
Each dot corresponds to either a data packet or an ACK packet

## Slide 35: High queueing delay causes unexpected TCP behavior
bytes in flight growing

## Slide 36: High queueing delay causes unexpected TCP behavior
Packet loss

## Slide 37: High queueing delay causes unexpected TCP behavior
Fast retransmission
Fast retransmission allows TCP to directly send the lost segment
to the receiver possibly preventing retransmission timeout

## Slide 38: High queueing delay causes unexpected TCP behavior
RTT: 262ms
RTO: 290ms
TCP uses RTT estimate to update retransmission timeout (RTO)
However, TCP does not update RTO based on duplicate ACKs
Duplicate ACKs

## Slide 39: High queueing delay causes unexpected TCP behavior
RTT: 356ms
RTO: 290ms
RTT > RTO, timeout!
Retransmission timeout happens, the congestion window drops to 1 segment, triggering slow start, hurting TCP performance
Slow start

## Slide 40: Prevalence of the slow-start problem
For all the large TCP flows with ≥ 1 packet loss, 20% of them suffer from the slow start problem, which consists of 12.3 % of all large TCP flows
In one case, a 3-minute flow even experience 50 slow starts, resulting in an average throughput of only 2.8Mbps, while the estimated bandwidth actually larger than 10Mbps

## Slide 41: Passive bandwidth estimation algorithm based on server-side traces
Import for understanding the network utilization efficiency of mobile applications
Active probing methods do not apply since the network condition is highly variable and it is impossible to launch measurement for all users

## Slide 42: Bandwidth estimation algorithm
Typical TCP data transfer

## Slide 43: Bandwidth estimation algorithm
Assume packet size is S,
sending rate between
t0 and t4 is

## Slide 44: Bandwidth estimation algorithm
From UE’s perspective,
the receiving rate for
these n − 2 packets is

## Slide 45: Bandwidth estimation algorithm
Typically, t2 is very close
to t1 and similarly for
t5 and t6

## Slide 46: Bandwidth estimation algorithm
We use TCP Timestamps
option to calculate
t6 − t2 (G is a constant
that can be inferred for
each client)
92.61% of the TCP flows have TCP Timestamps option enabled

## Slide 47: Bandwidth estimation algorithm
Using a sliding window, we obtain pairs of (Rsnd , Rrcv )
If a list of conditions about Rsnd and TCP flow characteristics are met, Rrcv is the estimated bandwidth
Using this algorithm, we are able to predict the available bandwidth for over 90% of the large downlink flows
We use local controlled experiments to validate, the error rate is 7.92%

## Slide 48: Bandwidth utilization by real applications in LTE
Median of bandwidth utilization ratio is 20%, and on average, the utilization ratio is 34.60%
For 71% of the large flows, the bandwidth utilization ratio is below 50%

## Slide 49: Bandwidth estimation timeline for two sample large TCP flows
LTE network has highly varying available bandwidth

## Slide 50: LTE bandwidth variability, RTT and TCP performance
Under small RTTs, TCP can utilize over 95% of the varying available bandwidth
When RTT exceeds 400∼600ms, the utilization ratio drops to below 50%
For the same RTT, higher variation leads to lower utilization
Long RTTs can degrade TCP performance in the LTE networks

## Slide 51: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource
Notes: In order to characterize the radio energy usage of cellular networks and mobile application,
we first need to understand the mechanisms of the radio interface that result in different power levels

## Slide 52: RRC state transitions in LTE
Notes: With the knowledge from the LTE specs and our local experiments,
we illustrate the LTE state machine and state transition procedures in this slide
There are two RRC states in LTE network, RRC_CONNECTED and RRC_IDLE.
Distinct states determine very different UE power consumption.

## Slide 53: RRC state transitions in LTE
RRC_IDLE
No radio resource allocated
Low power state: 11.36mW average power
Promotion delay from RRC_IDLE to RRC_CONNECTED: 260ms
Notes: In the RRC_IDLE state, there is no radio resource allocated and UE can’t receive/send any data.
UE is consuming very low average power at this state in the network interface, for example 11mW in our test device.
If there is any data transfer activity, there would be a state promotion from RRC_IDLE to a high power state: RRC_CONNECTED, and the measured promotion delay is 260ms in our test device, much smaller than that for 3G.

## Slide 54: RRC state transitions in LTE
RRC_CONNECTED
Radio resource allocated
Power state is a function of data rate:
  1060mW is the base power consumption
  Up to 3300mW transmitting at full speed
Notes: In the RRC_CONNECTED state, radio resource is allocated to a UE.
And the instant power level for UE is high, depending on data rate, it ranges from 1000mW to up to more than 3000mW when transmitting data at full speed.
If there is no data activity for some time, a timer would expire and it triggers the demotion from RRC_CONNECTED to RRC_IDLE

## Slide 55: RRC state transitions in LTE
Continuous Reception
Send/receive a packet
Promote to RRC_CONNECTED
Reset Ttail
Notes: Now, we will discuss the state transitions in LTE in more details
Initially, UE is in RRC_IDLE model, with no network resource allocated from the network.
When there is a packet to be sent or received, a state promotion from RRC_IDLE to RRC_CONNECTED would be triggered.
A timer called Ttail is reset at this time.
Ttail is the inactivity tail timer in LTE network, which controls how long UE stays in RRC_CONNECTED state after being idle

## Slide 56: RRC state transitions in LTE
Ttail stops
Demote to RRC_IDLE
DRX
Ttail expires
Notes: At RRC_CONNECTED state, after sending/receiving a packet, UE does not immediately go to RRC_IDLE.
Instead, UE keeps in RRC_CONNECTED state for some extra time. This extra time is called the tail time.
Ttail controls how long the tail time is.
When Ttail expires and UE demote to RRC_IDLE.

## Slide 57: Power trace of RRC state transitions
The data points are sampled and DRX in RRC_CONNECTED tail
is not obvious due to the low sampling rate
Notes: Next, we will talk about how we measure the power model for our analysis.
This figure shows the measured power trace of first uploading some data and then stays idle.
At time t1, when there is data to send, state promotion takes place and the power level jumps from very low to very high.
At time t2, data transmission starts and then depending on the instant data rate, the power level fluctuates.
At time t3, data transmission finished and the tail timer is started.
UE keeps in a high-power state until t4

## Slide 58: LTE power model (Verizon)
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: We notice that in the RRC_CONNECTED tail, for any DRX cycle, the power level of the off duration is 1060mW.
And the tail timer is measured to be 11.6seconds

## Slide 59: LTE consumes more instant power than 3G/WiFi in the high-power tail
Average power for WiFi tail
  120 mW
Average power for 3G tail
  800 mW
Average power for LTE tail
  1080 mW
Notes: We compare the instant tail power level of the three network types, since tail energy is the main source of wasted energy.
WiFi appears to be the least power consuming, only 120 mW.
3G tail has a high power level of 800 mW.
LTE has the even higher power level in RRC_CONNECTED mode, 1080 mW.
Considering that LTE tail timer is even longer than that for 3G in our measured network, more energy is wasted in the tail for LTE than 3G in that network.

## Slide 60: Power model for data transfer
A linear model is used to quantify instant power level:
  Downlink throughput td Mbps
  Uplink throughput tu Mbps
Notes: In addition to the power states, we also use a simple linear model to quantify the
instant power level based on the data rates in uplink and downlink.
The higher the throughput, the higher the power

## Slide 61: Power model for data transfer
A linear model is used to quantify instant power level:
  Downlink throughput td Mbps
  Uplink throughput tu Mbps
AT&T
Verizon
Notes: We measure the linear model in both Verizon and AT&T networks and they share similar patterns.

## Slide 62: Trace-driven modeling methodology
Real packet
traces collected
on smartphones
Network model
simulator
Adjusted packet timing and time series of RRC states
Power model
simulator
Calculated radio energy usage

## Slide 63: Trace-driven modeling methodology
Network model simulator
  Take binary packet trace files in libpcap format as input
  Remove existing state transition delays
  Apply a specific network model and adjust timestamps for some packets
  Output time series of packet arrival and RRC states
Power model simulator
  Takes the output of network model simulator as input
  Apply the corresponding power model and calculate radio energy usage

## Slide 64: Power model validation
< 6% error rate in evaluations with real applications
Power meter
directly measure
Real applications
running
Packet traces +
Trace-driven analysis
Notes: In addition to the power states, we also use a simple linear model to quantify the
instant power level based on the data rates in uplink and downlink.
The higher the throughput, the higher the power.
It’s simple yet validated to be effective and accurate, with the error rate for the predicted energy usage of real applications to be < 6%.

## Slide 65: Energy per bit comparison
LTE’s high throughput compensates for the promotion energy and tail energy
Transfer Size | LTE μ J / bit | WiFi μ J / bit | 3G μ J / bit
10KB | 170 | 6 | 100
10MB | 0.3 | 0.1 | 4
Total energy per bit for downlink bulk data transfer
Notes: In this table, we compare the energy per bit for the three networks in the downloading bulk data with different sizes.
For a small download of 10KB, LTE and 3G is clearly much more power consuming than WiFi, with LTE as 170 μJ/bit
However, when we download a large file of 10MB LTE’s high throughput compensates for the promotion energy and tail energy.
The energy per bit for LTE in this scenario is 0.3 μJ/bit, which is comparable to WiFi’s μJ/bit. While for 3G, it is much worse, with 4 μJ/bit.

## Slide 66: Energy per bit comparison
LTE’s high throughput compensates for the promotion energy and tail energy
Transfer Size | LTE μ J / bit | WiFi μ J / bit | 3G μ J / bit
10KB | 170 | 6 | 100
10MB | 0.3 | 0.1 | 4
Total energy per bit for downlink bulk data transfer
Small data transfer, LTE wastes energy
Large data transfer, LTE is energy efficient
Notes: So the high level observation for LTE network is that
It wastes energy for small data transfers,
But could become energy efficient for large data transfer.
For large data transfers, LTE has comparable energy efficiency compared with WiFi.

## Slide 67: UMICH data set
20 voluntary smartphone users for seven months
  Undergraduate and graduate students from 8 departments at University of Michigan
Data collected
  Full tcpdump packet traces
  Process name for sending/receiving each packet
  Screen status logger (1Hz)
  152GB in total

## Slide 68: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%
Notes: We future break down the energy usage into 4 components:
Promotion energy, data transfer energy, tail energy and idle energy.
We observe that tail energy takes up to 48% of the total energy for 3G and LTE network, while this problem does not exist in WiFi.

## Slide 69: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%
The tail problem is the key factor for LTE’s high energy consumption, similar to 3G networks
Notes: The tail problem is still the key factor for LTE high energy consumption, similar to 3G networks

## Slide 70: Screen-off traffic characterization: an interesting yet unexplored topic
Smartphone screen is switched on and off often (>50 times/day/user)
Screen status is a good heuristic for determining whether the user is actively interacting with the device
Notes: Screen-off traffic characterization is an interesting yet unexplored topic.
Here “screen-off” means switching the screen to off and putting the smartphone into standby mode, rather than meaning shutting down the phone

## Slide 71: Screen-off traffic characterization: an interesting yet unexplored topic
Smartphone screen is switched on and off often (>50 times/day/user)
Screen status is a good heuristic for determining whether the user is actively interacting with the device
Notes: and users do not want the battery drain too much when the screen is off

## Slide 72: Breakdown of packet count based on screen status
Chart: 
| Packet count
Screen-on | 55.13
Screen-off | 35.84
Unknown | 9.02
Unknown group: 9% of all packets, due to users
accidentally terminating screen status logger
50%
%
Notes: The breakdown of packet count based on screen status is shown as below

## Slide 73: Breakdown of packet count based on screen status
Chart: 
| Packet count
Screen-on | 55.13
Screen-off | 35.84
Unknown | 9.02
Unknown group: 9% of all packets, due to users
accidentally terminating screen status logger
50%
%
36% screen-off packets
Could be more given the unknown category
What is their energy and signaling impact?
Notes: Highlight that screen-off packet count is high

## Slide 74: Definition of a “burst”
A burst is a sequence of packets with inter-packet time ≤ BT, and leading/trailing gap > BT
BT is burst threshold selected empirically based on network RTTs, e.g. BT = 2s
> BT
> BT
≤ BT
…
≤ BT
Burst
Notes: In order to understand the signaling impact, we first define one term we use in this study is burst.
A burst is …
For the same number of packets, if there are more bursts, the traffic pattern is more scattered causing higher energy and signaling overhead.

## Slide 75: Screen-on and screen-off traffic comparison
Screen-off traffic has less packets/payload, but more bursts, which are smaller and shorter
Chart: 
| Packet number | Payload | Burst number
Screen-on | 55.13 | 64.31 | 22.2326
Screen-off | 35.84 | 27.26 | 65.2674
Unknown | 9.03 | 8.43 | 12.5
%
Notes: We first look at the aggregate traffic characteristics comparison between screen-on and screen-off traffic.
First, in terms of the % of all packets, …
Implication of these observations

## Slide 76: Does screen-off traffic matter for radio resource and energy?
Yes! Actually, screen-off traffic has higher impact than screen-on, though with less packets
Chart: 
| Screen-on | Screen-off | Unknown
Energy | 0.2218 | 0.5855 | 0.1927
Chart: Signaling overhead
| Screen-on | Screen-off | Unknown
Energy | 0.1487 | 0.5803 | 0.271
Notes: We then compare the radio and energy impact between screen-on and screen-off traffic
At least 59%, and unknown can even contribute to more screen-off energy

## Slide 77: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 78: RadioProphet: Intelligent Radio Resource Deallocation for Cellular Networks
Notes: We have done initial work on this project to demonstrate the effectiveness of the idea.
However, we have not fully implemented the RadioProphet system in real devices yet.

## Slide 79: Example feature selection – TCP flags
Notes: For SYN, PSH/ACK packets, clear indication of short burst

## Slide 80: Thank you!
Notes: Thank you and I’m glad to take questions!

## Slide 81: Backup slides

## Slide 82: 3GTest: Global 3G network performance measurement
Measure 3G network performance from users’ devices
Cross-platform
  iPhone OS, Android (Birjodh Tiwana) and Windows Mobile (Qiang Xu)
Global deployment
  60,000+ users, 140,000+ runs from 08/2009 to 04/2010
Notes: 3GTest is used for measuring the previous metrics globally
Talk about which is my part (iPhone + server design and implementation) and which are collaborator’s parts

## Slide 83: 3GTest collects representative results in many countries

## Slide 84: LTE Network characteristics
4GTest on Android
  Measures network performance with the help of 46 M-Lab nodes across the world
  3,300 users and 14,000 runs in 2 months 10/15/2011 ~ 12/15/2011
4GTest user coverage in the U.S.
Notes: To make such large-scale measurement, we developed and published an app called 4GTest in Android market.
In order to make sure that the Internet path does not become the bottleneck, 4GTest chooses the closest M-Lab nodes to connect to, which are distributed across the world.
Within 2 months of deployment, we collect data from more than 3000 users
Based on this figure, we can see that our data set has a reasonably good coverage in the United States.

## Slide 85: LTE Network characteristics
4GTest on Android
  Measures network performance with the help of 46 M-Lab nodes across the world
  3,300 users and 14,000 runs in 2 months 10/15/2011 ~ 12/15/2011
4GTest user coverage in the U.S.
Notes: To make such large-scale measurement, we developed and published an app called 4GTest in Android market.
In order to make sure that the Internet path does not become the bottleneck, 4GTest chooses the closest M-Lab nodes to connect to, which are distributed across the world.
Within 2 months of deployment, we collect data from more than 3000 users
Based on this figure, we can see that our data set has a reasonably good coverage in the United States.

## Slide 86: Tradeoffs of Ttail settings
Ttail setting | Energy Consumption | # of state transitions | Responsiveness
Long | High | Small | Fast
Short | Low | Large | Slow
Notes: Ttail is a very important parameter for both 3G and 4G networks.
It incurs tradeoffs between UE energy consumption, signaling overhead in the network quantified by the # of state transitions here
, and responsiveness
When Ttail is set to be a long value, UE consumes more energy, with smaller # of state transitions and fast responsiveness since UE spends more time in the RRC_CONNECTED state and there is less promotion delays.
When Ttail is set to be a short value, UE consumes less energy, incurring larger number of state transitions and more promotions delays
Later in this talk, we will explore in more details the impact of setting Ttail for LTE network.

## Slide 87: Smartphones are popular
Various smartphone platforms
Many applications
High speed network access
  3G (UMTS & EVDO)
  4G (LTE)

## Slide 88: Smartphone shipments prediction on 2009
Predicted on 2009: 2012 Global smartphone shipments 385 million

## Slide 89: Smartphone shipments booming
2012 Global smartphone shipments: 717 million
How about 2016?

## Slide 90: Design of 3GTest
Avoid personal identifiable information
http://mobiperf.com
Notes: Avoid personal identifiable information
Limit running time
Simple UI with one click to run
Leave users the option to run once or multiple times

## Slide 91: Key challenges of 3GTest design – public tool to measure 3G network performance
Adoptability
  User privacy
  Running time
  Ease of use
  Energy consumption
Data usefulness
  Metrics relevant to network applications
Notes: Talk about the challenges and our solutions
To extract important network metrics and understand network properties
To measure the network metrics globally to analyze commonalities and compare differences.

## Slide 92: What information is most relevant for 3GTest?
Smartphone
Local DNS server
Web server
example.com?
192.0.32.10
Get index.html
<html></html>
Ping to 1st hop
End-end ping
Notes: DNS performance
  Local DNS lookup time
TCP performance
  Throughput
  RTT
  Loss rate
Ping performance
  Latency to landmark servers
  Latency to the first hop

## Slide 93: Throughput comparison
CDF
T-Mobile:600kbps
AT&T
1Mbps
Notes: 1, variation within each carrier
2, common throughput values
3, ATT > T-Mobile

## Slide 94: RTT comparison
CDF
T-Mobile
450ms
AT&T
350ms
Notes: 1, variation within each carrier
2, common RTT values 400ms (higher than Internet values)
3, ATT > T-Mobile (T-Mobile has high RTT)

## Slide 95: Retransmission rate comparison
CDF
T-Mobile
AT&T
Notes: 1, common retransmission values
2, UMTS vs. EVDO (possibly due to link-layer retransmission
Link-layer retransmission for low loss rate

## Slide 96: TCP retransmission rate comparison across carriers
TCP retransmission rate is low (0% selected)
T-Mobile and AT&T’s median of TCP retransmission rate is 0%, while Sprint and Verizon have 0.7%
Notes: Loss rate

## Slide 97: Ping to the first hop

## Slide 98: Ping to end server

## Slide 99: Time of day effect on network performance

## Slide 100: JavaScript execution comparison (2009)
PC
80X (CPU <10X)
Notes: Background: choose to use JavaScript because it is the most common scripts which require client processing
PC vs. smartphone difference is big (js is expensive on smartphones, content providers need to optimize contents)
Difference among different smartphones are big
Possible reasons include CPU speed difference and JS engine software performance difference

## Slide 101: Interesting questions about LTE
To users: what is the end performance?
  Network performance, such as RTT and throughput, how it compares with WiFi, 3G and WiMAX, etc.
  Energy efficiency affecting battery life, is LTE more power efficient than 3G or WiFi?
To ISPs: what is the impact of configuring LTE-related parameters on UE power saving, and delay/signaling overhead?
To OS/application developers: what is the performance bottleneck of applications in LTE network, CPU or network speed?
Notes: Given the previous discussion on LTE networks, in this study,
We raise some interesting questions about LTE network that are of interest of users, mobile ISPs and OS/application developers.
For users, they are interested to understand the network performance of LTE network and how it compares to other technologies, such as 3G, WiFi, WiMAX, etc.
For ISPs, the impact of configuring LTE-related parameters on energy saving and delay and signaling overhead is yet to be studied.
For OS and application developers, we want to study how the new LTE network would affect the application design
And what the is the performance bottleneck of mobile applications is it CPU or network speed.
(Merge with the first transition slide)

## Slide 102: RRC state transitions in LTE
DRX: Discontinuous Reception
Listens to downlink channel periodically for a short duration and sleeps for the rest time to save energy at the cost of responsiveness
Notes: Discontinuous reception, or DRX, is an important feature in LTE for energy saving purpose.
Instead of continuous monitoring downlink channel, in DRX, UE only listens to downlink channel periodically for a short duration, and sleeps for the rest time to save energy at the cost of responsiveness.

## Slide 103: Discontinuous Reception (DRX): micro-sleeps for energy saving
In LTE 4G, DRX makes UE micro-sleep periodically in the RRC_CONNECTED state
  Short DRX
  Long DRX
DRX incurs tradeoffs between energy usage and latency
  Short DRX – sleep less and respond faster
  Long DRX – sleep more and respond slower
In contrast, in UMTS 3G, UE is always listening to the downlink control channel in the data transmission states
Notes: We explain DRX in more details here.
In LTE 4G networks, DRX makes UE micro-sleep periodically in RRC_CONNECTED state.
There are two types of DRX in RRC_CONNECTED, Short DRX and Long DRX.
Different types of DRX incurs tradeoffs between battery saving and latency.
Short DRX sleeps slightly less with smaller energy saving and respond faster
Long DRX, sleeps more with more energy saving and respond slower.
The DRX in the data transmission state is one major difference between 3G and LTE.
In UMTS 3G networks, during the data transmission states, UE is continuously listening to the downlink control channel

## Slide 104: DRX in LTE
A DRX cycle consists of
  ‘On Duration’ - UE monitors the downlink control channel (PDCCH)
  ‘Off Duration’ - skip reception of downlink channel
Ti: Continuous reception inactivity timer
  When to start Short DRX
Tis: Short DRX inactivity timer
  When to start Long DRX
Notes: Now let’s look at DRX with a microscope.
DRX is periodic and each DRX cycle consists of
‘On Duration’ during which UE monitors the downlink control channel
‘Off Duration’ during which UE can sleep and skip the reception of downlink channel for battery saving purpose.
The On Duration is typically much smaller than the Off Duration so as to make effective energy saving
First, let’s start from the red dots where the UE starts transferring data.
Every time a packet is sent or received, the continuous reception inactivity timer Ti is started.
And when Ti expires, UE starts short DRX.
Then the short DRX inactivity timer Tis starts and when Tis expires without seeing any data, long DRX starts.

## Slide 105: RRC state transitions in LTE
Continuous Reception
Send/receive
a packet
Reset Ti
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 106: RRC state transitions in LTE
Short DRX
Ti stops, Tis starts
Ti expires
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 107: RRC state transitions in LTE
Continuous Reception
Send/receive
a packet
Reset Ti, stops Tis
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 108: RRC state transitions in LTE
Long DRX
Tis stops
Tis expires
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 109: RRC state transitions in LTE
Reset Ti
Continuous Reception
Send/receive
a packet
Notes: Add T_pro, have another slide showing all numbers
Each time data is sent/received Ti and Ttail are reset, Tis is when Short DRX starts, Ti + Tis << Ttail, animation to show how Timers are set (only appear after started)

## Slide 110: Power trace of DRX in RRC_CONNECTED
Notes: This figure is a zoom-in view of the power traces in RRC_CONNECTED model.
We can observe an obvious periodic behavior of DRX and around every 40ms
UE wakes up to check the downlink control channel for a very short period and goes back to sleep again.
To point to the difference

## Slide 111: One way delay and impact of packet size
LTE uplink one way delay (OWD) is larger than that of downlink
RTT in LTE is more sensitive to packet size than WiFi, mainly due to uplink OWD

## Slide 112: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: We measure the LTE power model with our test device and Monsoon power meter.
And we take the average with repeated samples.
All the energy are measured with screen turned off.

## Slide 113: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: As a reference for comparison, we measure the power level when the device is doing nothing but with the screen 100% on.
The power level is around 850 mW.

## Slide 114: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
Notes: For DRX on duration, the power level is even higher, up to 1680mW.

## Slide 115: LTE power model Verizon
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples
P(on) – P(off) = 620mW, DRX saves 36% energy in RRC_CONNECTED
High power levels in both On and Off durations in the DRX cycle of RRC_CONNECTED
Notes: We make two interesting observations out of this table.
First, we notice that the DRX on duration has a higher power level than that of the off duration and
The gap between on and off is 620mW. This large gap allows the DRX to save 36% energy in RRC_CONNECTED state.
So DRX is effective.
Second, both on and off durations in the DRX cycle of RRC_CONNECTED, have high power levels.
So even though DRX helps save significant amount of energy, LTE still has high energy consumption in RRC_CONNECTED state.
This observation suggests that the high-power tail might still be a key source of energy inefficiency of LTE network as it is in 3G network.

## Slide 116: Power model for data transfer
A linear model is used to quantify instant power level:
  Uplink/downlink throughput tu/td (Mbps)
< 6% error rate for predicting energy usage of 5 real applications

## Slide 117: Energy per bit comparison
For large data transfer with maximum rate, LTE’s energy efficiency is comparable with WiFi, due to LTE’s high downlink throughput
Notes: Add comparison between WiFi and LTE’s absolute power levels.
The result in this slide is not general, because WiFi has < 6Mbps.
Probably remove this figure.
Add back this slides, remove the figure, put numbers.
Useful for bundle the data transfer

## Slide 118: LTE power model AT&T (New Jersey)

## Slide 119: LTE power model AT&T (Michigan)

## Slide 120: User trace based analysis
UMICH data set
  Collected from 20 volunteer smartphone users for five months, totaling 118GB
  Contains packet traces including full payload
Trace-driven modeling methodology
  Network model simulator
    Simulates network states, such as RRC state transitions
  Power model simulator
    Calculates power usage based on the network states
Notes: The approach we took for such comparison is the user trace based simulation analysis.
The data set we have is collected from 20 volunteer smartphone users for 5 months.
It contains packet traces with full payload.
We feed these traces into our network model simulator which simulates RRC state transitions
and power model simulator which is used to calculate energy usage based on the different network states.
This approach is not perfect since it is inherently challenging to replay user behaviors in different networks, especially when remote entities have been involved.
However, we believe that this approach provides a representative comparison for the energy efficiency of different networks.

## Slide 121: Comparing total energy of all user traces via simulation in LTE/3G/WiFi
Total energy usage
  LTE/WiFi ≈ 23 3G/WiFi ≈ 15
Notes: We first compare the total energy usage of all user traces.
In this figure, blue bars represent the energy ratio of LTE and WiFi
And red bars represent the energy ratio of 3G and WiFi.
In aggregate, we observe that LTE consumes up to 23 times the energy of WiFi, while 3G is 15 times of WiFi.
Across users, the ratio changes, but the overall pattern is consistent for all users.

## Slide 122: Design tradeoff in smartphone measurement
User coverage vs. collected information
User coverage
More info
Fewer users
Less info
More users
Collected information
Speedtest.net
FCC’s broadband test
Liu, MobiCom 2008
Zhong, HotMetrics 2010
Willkomm, DySPAN 2008
Our study
Notes: Discuss tradeoff: jailbroken / user privacy

## Slide 123: Key challenges of web performance analysis
Multiple factors have impact
  Network condition
  Client settings
  Server configurations
  Content differences
Lack of low-level information and access
  No visibility into link layer
  Difficult to instrument client OS and application
  No access to public web servers
Notes: 1 because various factors have joint impact

## Slide 124: How to isolate impact of individual factor?
Vary one factor at a time
  Network condition
    Simulate cellular network with WiFi
  Client settings
    Control TCP concurrency
  Server configurations
    Change compression mode and server parallelism
  Content difference
    Host static website snapshots locally
Notes: Present our solutions
each of which solves one problem in the problem statement
assume WiFi's performance is predictable due to a lack of contention.
WiFi has higher performance so you can create bottlenecks to emulate 3G.

## Slide 125: How to identify performance bottlenecks?
TCP flow analysis technique to break down page load time
  DNS lookup time
  TCP handshake time
  TCP idle time
  TCP transfer time
index.html
logo.png
Time
Notes:   DNS lookup time – local DNS server lookup time
  TCP handshake time - RTT
  TCP idling time - client execution time
  TCP transfer time - network performance & server delay

## Slide 126: Controlled experiment setup
Platform
Web browsing
Notes: Talk about the carrier and devices used for controlled experiments
20 URLs include mail, search engines, social networks, maps.

## Slide 127: Data set studied
Collected from 20 volunteers in 5 months
  May 2011 ~ Oct 2011, Android 2.2 smartphones
Full packet payload and process association is collected
  131.49 millions packets
  80.03GB payload
Screen on/off status with sampling rate of 1Hz
Notes: To study the screen-off traffic, we use a data set …
…
When we first got the data set, we are curious how many packets are generated during the screen-off stage

## Slide 128: Radio Resource Control (RRC) state machine
Tail
Time
Promotion
Power
Transfer
the packet
A packet to
transfer
Tail timer
starts
Tail timer
expires
Notes: To understand the energy and signaling impact of network traffic, we review the Radio resource control state machines in cellular networks, or RRC state machines.

## Slide 129: How does traffic pattern affect energy and radio resource?
Scattered traffic consumes more energy and radio resource than Gathered traffic
Scattered
traffic
Gathered
traffic
Time
Power
Notes: Radio resource control state machine is important in determining cellular radio resource usage and UE energy consumption.
We need to understand two terms used in this study.
Promotion is …
Tail is defined to be the period that UE continus to stay in the high-power state

## Slide 130: Top screen-off applications based on packet count
Application category | screen-off packets / total packets
Homescreen widget | 3.80%
Multimedia streaming | 3.30%
Utility | 2.69%
Multimedia streaming | 2.66%
Multimedia streaming | 2.37%
Utility | 2.07%
Social network | 1.95%
News | 1.94%
Email | 1.33%
Notes: We then explore which application or progress generates most of the screen-off packets
Group app names into category
But having a large number of packets does not mean a big impact on energy consumption and signaling overhead

## Slide 131: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Notes: We further investigate the energy impact of top screen-off processes.
In the table, red bar represents the energy overhead, blue bar represents the burst count.
We can observe clear differences among applications.
We classify the applications to be 2 groups, based on their traffic pattern, the scattered group and the gathered group.
Comparing the two groups, we notice that although the total number of packets are comparable, scattered group includes significantly higher number of bursts incurring high energy impact.

## Slide 132: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Notes: Comparing these two applications

## Slide 133: Energy impact of top screen-off applications
Scattered group has more bursts than
Gathered group, incurring higher energy impact
Application category | Group | 
Homescreen widget | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Multimedia streaming | Gathered | 
Multimedia streaming | Gathered | 
Utility | Scattered | 
Social network | Scattered | 
News | Scattered | 
Email | Scattered | 
Chart: 
| App 9 (Gathered) | App 8 (Gathered) | App 7 (Gathered) | App 6 (Gathered) | App 5 (Gathered) | App 4 (Gathered) | App 3 (Scattered) | App 2 (Gathered) | App 1 (Gathered)
Burst count | 0.036026 | 0.045695 | 0.069518 | 0.014598 | 0.00049183 | 0.002787 | 0.021599 | 0.0018102 | 0.0020151
Energy impact | 0.0118 | 0.0301 | 0.0525 | 0.0096 | 0.0008 | 0.0013 | 0.0163 | 0.0012 | 0.0034
Traffic pattern has significant impact on resource consumption
    1.95% packets + 5% energy (Scattered)
    2.37% packets + 0.1% energy (Gathered)
Notes: For example, the screen-off traffic of one social network app consumes 5% of the total energy of applications in both screen-on and screen-off stages.
However, another multimedia streaming app with more screen-off packets consumes only 0.1% of the total energy.

## Slide 134: Object bundling
Bundling objects requested by the same client and transferring in one single bundle helps improve energy and network efficiency
Where to bundle? Server? Cellular core network? Cell tower?
How to bundle? Proactively or on demand?
How to quantify benefits?

## Slide 135: Screen-aware traffic optimization
Apply more aggressive settings to screen-off traffic
  Reason 1: high energy and signaling impact
  Reason 2: traffic pattern is more “scattered”
  Reason 3: less user interaction and more tolerance in delay
Notes: Given that the screen-off traffic consumes significant amount of UE energy and radio resources,

## Slide 136: Case study: screen-aware fast dormancy
Fast dormancy reduces the tail length by actively notifying the network for early demotion
Fast dormancy
136
Time
Power
Default tail timer
Fast dormancy
tail timer
Notes: As case study, we first study fast dormancy, which is a technique to allow UE to demote to low power state faster by actively notifying the network.

## Slide 137: Case study: screen-aware fast dormancy
Fast dormancy reduces the tail length by actively notifying the network for early demotion
Fast dormancy
137
Time
Power
Screen-aware fast dormancy: a shorter tail timer for screen-off traffic
For the same signaling overhead, screen-aware fast dormancy increases energy saving by 15% compared with basic fast dormancy

## Slide 138: Summary
Screen-off traffic incurs more energy overhead, with fewer packets and less payload than screen-on traffic
Screen-aware optimization improves the resource efficiency and is simple to implement
Other screen-aware traffic optimization techniques studied in the paper, e.g., batching