## Slide 1: Performance and Power Characterization of Cellular Networks and Mobile Application Optimizations
Junxian Huang
University of Michigan
April 25, 2013

## Slide 2: Smartphone Ecosystem
Customer
Smartphone
Vendors
Application
Developers
Mobile
Carriers
Content
Providers
Slow!
Out of battery!

## Slide 3: Key Motivations
Performance and power characteristics of cellular networks and smartphone applications are not well studied
  especially for the new LTE networks
Many smartphone applications are not well designed with inefficient use of network, radio and power resources
  mainly due to the unawareness of the cellular specific characteristics

## Slide 4: My Research Goal
Challenges
  Multiple entities involved
  The solution needs to be general and practically deployable
  Requires evaluation using real cellular workload
To design practical and effective methods to characterize the resource utilization (bandwidth, energy, radio resource…) in cellular networks and improve the mobile application design.

## Slide 5: Thesis Statement
We devise a suite of systematic methodology and tools to accurately measure the performance and power characteristics of cellular networks (both 3G and the LTE 4G networks) as well as the mobile applications, and to optimize the mobile application design based on such knowledge

## Slide 6: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 7: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 8: Design Goals of MobiPerf
Measure most relevant network characteristics of cellular networks
Measurement results not be affected by any external factors
Attract a large number of users covering different carriers and geographical regions
Benefit the research community in terms of both tool and data

## Slide 9: Cellular Network Metrics
DNS (domain resolution)
  Local DNS response time
TCP
  Common TCP metrics: downlink/uplink throughput, round-trip time (RTT), packet loss rate, etc.
  For TCP throughput test, we choose the closest nodes among the 120+ global M-Lab nodes and use parallel TCP connections
Smartphone
Web server
Local DNS server

## Slide 10: Cellular Network Metrics
Ping (Impact of diverse Internet servers)
  Ping A: Ping latency to the first responsive IP hop
  Ping B: Ping latency to landmark servers at diverse Internet locations
Ping A
Ping B

## Slide 11: http://mobiperf.com

## Slide 12: Coverage of MobiPerf Data
  70K+ users 200K+ runs 84 carriers 147 countries

## Slide 13: MobiPerf Benefits the Research Community
Open source
  https://github.com/Mobiperf/MobiPerf
  Other researchers can easily add modular measurement tasks into MobiPerf tool
Open data
  gs://openmobiledata_public (Google storage)
Recognition
  In 2011, People's Choice Award and Open Internet App Reward in the FCC Open Internet Apps Challenge

## Slide 14: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 15: Smartphone web browsing is complicated
Smartphone
Local DNS server
Web server
DNS lookup
Content customization
TCP handshake
TCP data transfer
1
2
4
Server configuration
Client configuration
HTML rendering & JavaScript execution
5
Network condition
Server processing delay
3

## Slide 16: Key challenges of web performance analysis
Multiple factors have joint impact
  Network condition
  Client settings
  Server configurations
  Content differences
Lack of low-level information and access
  No visibility into link layer
  Difficult to instrument client OS and application

## Slide 17: How to isolate impact of individual factor?
Vary one factor at a time
  Network condition
    Simulate cellular network with WiFi via iptables
  Client settings
    Control TCP concurrency
  Server configurations
    Change compression mode and server parallelism
  Content difference
    Host static website snapshots locally

## Slide 18: How to identify performance bottlenecks?
TCP flow analysis technique to break down page loading time
  DNS lookup time
  TCP handshake time
  TCP idle time
  TCP transfer time
index.html
logo.png
Time
T
T1
T2
ta
tb

## Slide 19: Web browsing breakdown
Chart: 
| G2 / simple | HTC / simple | G2 / complex | HTC / complex
DNS lookup | 0.8 | 1.5 | 0.9 | 1.6
TCP handshake | 1.1 | 1.3 | 1.2 | 1.4
TCP transfer | 4.5 | 5 | 8.5 | 10
TCP idle | 5 | 7.5 | 6 | 18
Web browsing performance bottlenecks
  Client execution (TCP idle time)
  Network transfer (TCP transfer time)
TCP idle time
TCP transfer time
Page loading time (seconds)

## Slide 20: Lessons from web browsing performance study
Performance bottlenecks of web browsing
  Client execution
  Data download (less critical for LTE)
Higher concurrency and content compression significantly improves performance
Content customization is beneficial
  Data URL scheme
  Minification
  Redirection reduction

## Slide 21: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 22: LTE is New, Requires Exploration
4G LTE (Long Term Evolution) is future trend
  Initiated by 3GPP in 2004
    100Mbps DL, 50Mbps UL, <5ms latency
  Entered commercial markets in 2009 and now available in more than 10 countries

## Slide 23: Motivations
LTE has not been extensively studied empirically in a commercial network setting
Study how network resources are utilized across different protocol layers for real users
Evaluate the benefits of increased bandwidth for mobile applications and essential network protocols to identify their limitations

## Slide 24: LTE network topology of the studied carrier

## Slide 25: LTE network topology of the studied carrier
Data collection point

## Slide 26: Data set studied
Data set statistics
  Covering a fixed set of 22 eNBs at a large metropolitan area in the U.S.
  Over 300,000 users
  3.8 billion packets, corresponding to 3 TB of LTE traffic
  Collected over 10 consecutive days
Data contents: packet header trace consisting of
  IP and transport-layer headers
  A 64-bit timestamp for each packet
  No payload data is captured except for headers of HTTP

## Slide 27: Queueing delay
Large buffers in the LTE networks may cause high queuing delays
Bytes in flight – unacknowledged TCP bytes

## Slide 28: High queueing delay causes unexpected TCP behavior
When one LTE user is downloading data …
Each dot corresponds to either a data packet or an ACK packet

## Slide 29: High queueing delay causes unexpected TCP behavior
bytes in flight growing

## Slide 30: High queueing delay causes unexpected TCP behavior
Packet loss

## Slide 31: High queueing delay causes unexpected TCP behavior
Fast retransmission
Fast retransmission allows TCP to directly send the lost segment
to the receiver possibly preventing retransmission timeout

## Slide 32: High queueing delay causes unexpected TCP behavior
RTT: 262ms
RTO: 290ms
TCP uses RTT estimate to update retransmission timeout (RTO)
However, TCP does not update RTO based on duplicate ACKs
Duplicate ACKs

## Slide 33: High queueing delay causes unexpected TCP behavior
RTT: 356ms
RTO: 290ms
RTT > RTO, timeout!
Retransmission timeout happens, the congestion window drops to 1 segment, triggering slow start, hurting TCP performance
Slow start

## Slide 34: Prevalence of the slow-start problem
For all the large TCP flows with ≥ 1 packet loss, 20% of them suffer from the slow start problem, which consists of 12.3 % of all large TCP flows
In one case, a 3-minute flow even experience 50 slow starts, resulting in an average throughput of only 2.8Mbps, while the estimated bandwidth actually larger than 10Mbps

## Slide 35: Passive bandwidth estimation algorithm based on server-side traces
Import for understanding the network utilization efficiency of mobile applications
Active probing methods do not apply since the network condition is highly variable and it is impossible to launch measurement for all users

## Slide 36: Bandwidth estimation algorithm
Typical TCP data transfer

## Slide 37: Bandwidth estimation algorithm
Assume packet size is S,
sending rate between
t0 and t4 is

## Slide 38: Bandwidth estimation algorithm
From UE’s perspective,
the receiving rate for
these n − 2 packets is

## Slide 39: Bandwidth estimation algorithm
Typically, t2 is very close
to t1 and similarly for
t5 and t6

## Slide 40: Bandwidth estimation algorithm
We use TCP Timestamps
option to calculate
t6 − t2 (G is a constant
that can be inferred for
each client)
93% of the TCP flows have TCP Timestamps option enabled

## Slide 41: Bandwidth estimation algorithm
Using a sliding window, we obtain pairs of (Rsnd , Rrcv )
If a list of conditions about Rsnd and TCP flow characteristics are met, Rrcv is the estimated bandwidth
We use local controlled experiments to validate, the error rate is < 8%
Using this algorithm, we are able to estimate the available bandwidth for over 90% of the large downlink flows

## Slide 42: Bandwidth utilization by real applications in LTE
Median of bandwidth utilization ratio is 20%, and on average, the utilization ratio is 35%
For 71% of the large flows, the bandwidth utilization ratio is below 50%
Reasons for underutilization
  Small object size
  Insufficient receiver buffer
  Inefficient TCP behaviors

## Slide 43: Bandwidth estimation timeline for two sample large TCP flows
LTE network has highly varying available bandwidth

## Slide 44: LTE bandwidth variability, RTT and TCP performance
Under small RTTs, TCP can utilize over 95% of the varying available bandwidth
When RTT exceeds 400∼600ms, the utilization ratio drops to below 50%
For the same RTT, higher variation leads to lower utilization
Long RTTs can degrade TCP performance in the LTE networks

## Slide 45: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 46: Radio Resource Control (RRC) state transitions in LTE

## Slide 47: RRC state transitions in LTE
RRC_IDLE
No radio resource allocated
Low power state: 11.36mW average power

## Slide 48: RRC state transitions in LTE
RRC_CONNECTED
Radio resource allocated
Power state is a function of data rate:
  1060mW is the base power consumption
  Up to 3300mW transmitting at full speed

## Slide 49: RRC state transitions in LTE
Continuous Reception
Send/receive a packet
Promote to RRC_CONNECTED
Reset Ttail

## Slide 50: RRC state transitions in LTE
Ttail stops
Demote to RRC_IDLE
DRX
Ttail expires

## Slide 51: Power trace of RRC state transitions
The data points are sampled and DRX in RRC_CONNECTED tail
is not obvious due to the low sampling rate

## Slide 52: LTE power model (Verizon)
Measured with a LTE phone and Monsoon power meter, averaged with repeated samples

## Slide 53: Trace-driven modeling methodology
Real packet
traces collected
on smartphones
Network model
simulator
Adjusted packet timing and time series of RRC states
Power model
simulator
Calculated radio energy usage

## Slide 54: Power model validation
< 6% error rate in evaluations with real applications
Power meter
directly measure
Real applications
running
Packet traces +
Trace-driven analysis

## Slide 55: UMICH data set
20 voluntary smartphone users for seven months
  Undergraduate and graduate students from 8 departments at University of Michigan
Data collected (152GB in total)
  Full tcpdump packet traces
  Process name for sending/receiving each packet

## Slide 56: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%

## Slide 57: Energy consumption break down
Tail energy dominates LTE energy consumption, similar to 3G
The total energy for different networks and users is normalized to be 100%
The tail problem is the key factor for LTE’s high energy consumption, similar to 3G networks

## Slide 58: Roadmap
MobiPerf: characterizing cellular network performance
Anatomizing smartphone application performance
An In-depth Study of LTE
Characterizing Radio Energy Usage
RadioProphet: Optimizing Smartphone Energy and Radio Resource

## Slide 59: Radio Resource Control (RRC) State Machine
Tail
Time
Promotion
Power
Data transfer
A packet to
transfer
Tail timer
starts
Tail timer
expires

## Slide 60: Fast Dormancy (FD)
Fast dormancy reduces the tail length by actively notifying the network for early demotion
Fast dormancy
60
Time
Power
Default tail timer
Fast dormancy
tail timer

## Slide 61: Problem with the Naïve Fast Dormancy
Extra promotion overhead
  UE energy and delay overhead
  Signaling overhead
    32 radio messages exchanged between UE and cell tower for promotion
No FD
FD
Time
Power

## Slide 62: RadioProphet: Intelligently Invoke FD
No FD
FD
Time
Power
RadioProphet

## Slide 63: Definition of a “burst”
A burst is a sequence of packets with inter-packet time ≤ BT, and leading/trailing gap > BT
BT is burst threshold selected empirically based on network RTTs, e.g. BT = 2s
> BT
> BT
≤ BT
…
≤ BT
Burst
Inter-burst time (IBT)

## Slide 64: RadioProphet: Intelligent Radio Resource Deallocation for Cellular Networks

## Slide 65: Inter-Burst Time (IBT) Prediction
Traffic features
  Packet direction, port, packet length, protocol, TCP flags, application ID
Machine learning algorithms
  Naïve Bayes
  Regression tree
  Classification tree
  Ensemble boost
  … etc.

## Slide 66: Example Feature Selection – TCP Flags

## Slide 67: Implementation and Evaluation
Data collector
  Modified tcpdump cross-compiled for Android
  Collect traffic for prediction
  < 2% CPU overhead (energy overhead < 1% tail energy)
IBT prediction framework
  Weka machine learning library ported to Android
  Average model training time 200ms, prediction time 0.1ms (energy overhead < 1% tail energy)
  Best accuracy for all users in the UMICH data set is 86%
Overall performance
  Energy saving: 59% of radio energy (20% ~ 30% total energy)
  Signaling overhead reduction: 57% comparing with default FD

## Slide 68: Summary and Future Agenda
Optimizing cellular network and power resource usage for mobile applications is important and requires further study
MobiPerf
  A more general mobile measurement platform to better benefit the research community in both the tool and data
  Longitudinal study of the evolution of cellular networks
RadioProphet
  To consider more TCP- and application-layer context to improve prediction accuracy
  Public deployment and OS integration

## Slide 69: Thank you!